## Slide 1: Remember Architectural Basics
By the time you complete this power point you should be familiar with:
Architectural symbols: The language of architecture
Why are construction documents comprised of different views
Visual communication methods
Tools used by architects and designers

## Slide 2: Architectural Symbols
The language of symbols offers a symbolic representation of building elements used on drawings showing their placement in relationship to other building elements.

## Slide 3: Floor plan with symbols

## Slide 4: Construction Documents & Drawings
These views include:
Section Views
Detail Views
Floor Plans
Elevations
Set of documents that show details about the construction and design of the structure

## Slide 5: Section View
A portion of a set of construction plans that shows a section or cut through of the structure. Imagine how a slice of a 5 layer cake looks. You see the layers and the frosting in-between. In a plan view, you see the composition of the floor, wall and roof framing systems.
“How would this be helpful for the person constructing the building?”

## Slide 6: Section View

## Slide 7: Detail View
This view shows a detail of the plan that has been magnified for closer inspection of the construction elements.

## Slide 8: Detail View
What details are
made clearer with this detail view of a handrail for a theater?

## Slide 9: Floor Plan
This plan shows the location of walls, windows, doors and fixtures in a structure
It is drawn from a birds eye or overhead view as though the roof had been removed.

## Slide 10: Elevations
A 2-D drawing of a wall from floor to ceiling. It will include structural elements such as doors, windows and fixtures. There are also exterior elevations that show a single wall of the outside of a dwelling.

## Slide 11: Elevations

## Slide 12: Architectural Tools
These tools are used by architects, designers and engineers to create accurate plans for the construction of buildings. They include:
T-square
Triangle
Architectural Scale
Template

## Slide 13: T-square (straightedge)
This tool helps designers when hand drawing to create accurate horizontal and vertical lines.
“As your teacher holds up the T-square, how do you think it works?”

## Slide 14: Triangle
These tools are pre-calibrated at specific angles to aid the designer in creating accurate drawings. Adjustable angles are hinged for customized angle creation.
“How do you think you would use the T-square and triangle together to create accurate horizontal, vertical and diagonal lines?”

## Slide 15: Architectural Scale
A measuring device calibrated at various scales to assist in the creation of scaled drawings. It consists of 12 scales.

## Slide 16: Template
A thin plastic sheet with cutouts that can be traced to provide the accurate shape and size of objects to be drawn into a floor plan. There are several varieties that include:
Furnishings
Bath Fixtures
Kitchen Fixtures
Structural
“As you view a template, what does it remind you of? Ever traced letters using a stencil?”

## Slide 18: Tracing Paper
A strong transparent used to create drawings, designs and tracing.
Often referred to as trash paper.

## Slide 19: CADD
Computer aided drafting and design
This type of software speeds the process of creating plans that are accurate and industry accepted. Modifications are easy to make and many have a 3-D option for viewing the drawing in perspective.

## Slide 20: Types of CADD programs
Consumer friendly versions that are free on-line:
Ethan Allen
West Elm
Bassett
Pottery Barn
Homestyler*
Roomstyler
Room Planner*
Floorplanner
Cool House Plans
ePlans
Fenton Commercial Plans
House Designers
Southern Living House Plans
Stockton Designs
The House Plan Shop
IKEA
*These versions offer more challenge to the user
Professional versions:
Revit
AutoCad

## Slide 21: Architectural Renderings

## Slide 22: What is a rendering?
The visual enhancement of any drawing through color, value, and texture.
Notes: Bring a three-dimensional human quality to two-dimensional objects

## Slide 23: What do renderings do?
Offers the client the ability to visualize what the space will look like before actual construction begins.

## Slide 24: What should you render?
You can render just about anything.
Floor plans, wall elevations, and exterior views of a home are popular renderings.

## Slide 25: Rendering Media
Most popular rendering media include:
  Colored pencil
  Graphite pencil
  Watercolor
  Felt-tip markers

## Slide 26: Note to me: I think I’m ready to learn more since I know about the basics!!!
so…What’s next?