## Slide 1: Kitchen Design
Interior Design I
Objective 3.03

## Slide 2: Evolution of Kitchen Design
Kitchens of the past were built for individual users
Today kitchens are used as gathering spaces for a wide variety of family activities.
Kitchens should be based on individual needs not trends.
Determine the needs of the kitchen before you determine the layout.

## Slide 3: Work CENTERS for kitchen activities:
    Storage
      Refrigerator, cabinets, & pantry for storing food, dishes, & utensils
    Food Preparation
      Has continuous main work counter space and needed small appliances
    Cooking
      Cooking pots and pans, stove, microwave
    Clean Up
      Sink and dishwasher, recycling and waste management
Notes: Avoid designing kitchens where traffic has to walk through the prep zone, keep countertops continuous in the food prep area, plan for extra GFCI electric outlets, lighting is extremely important in kitchens, place the largest countertop between the sink and the range, place refrigerator close to the sink, do not put tall counter obstructions between sink and stove.
Storage: Two types of storage: Wet goods, and dry goods. Not everyone will have a separate pantry, additional places might include lazy susans in cabinets, swing out pantries, and or spice racks near the stove. The refrigerator needs at least 18 inches counter space beside it on the same side as the handle.
Food Preparation: usable counter space is the most important piece of this center. Try storing appliances somewhere besides the countertop to give you more space, especially in a small kitchen. Need at least 36 inches wide and 24 inches deep of continuous counter space.
Cooking: If possible having built-in microwaves, pot racks and utensils nearby will help stream line cooking. Need at least 12 inches of counter space on one side and 15 inches on the other side. Make sure you have properly vented cooktop. Do not place the cooktop under a window.
Cleaning: dishwashers should be near the sink, as well as trash & recycle bins. Should be located adjacent to or across from the cooking surface. Need at least 18 inches on one side of the sink and 24 inches on the other side. Dishwasher needs to be within 36 inches of the sink. Keep cleaning supplies close but out of the reach of children or pets.
You want to make sure that all outlets in the kitchen have GFCI protection. You also want to make sure that kitchens have proper lighting and all work spaces are well lit.

## Slide 4: Work Triangle
  Determined by the placement of the sink, refrigerator and range.
The total walking distance between refrigerator, sink & range should be between 12 to 26 feet in length.
Any one side should be between 4-9 ft.
Kitchens may have more than one work triangle.
Notes: The work triangle should not be interrupted by traffic or cabinetry.
Many kitchens now have multiple work zones that include additional areas such as a separate oven, prep sink, microwave, or enough room for a second cook.
Determine how many people will be cooking at one time to help determine how large your kitchen needs to be and how many work triangles you may need.
Ideally you don’t want anyone not cooking to have to walk through the work triangle while you are preparing foods.

## Slide 5: ADA Guidelines for Kitchen Design
Clearance for movement: 40 inches for pass-through kitchens, 60 inches for u-shaped kitchens
Work surface: section of lower countertops between 28-34 inches above floor, have at least one space that is 30 inches wide to wheel under
Sink: 28-34 inches off floor, no base cabinet obstruction, insulate pipes
Storage: store most used items between 15 inches and 48 inches
Appliances: have a clearance space of 30-48 inches in front, appliance doors should not interfere with each other
Cooktop: need 12-15 inch counter space on both sides of cooktop

## Slide 6: One Wall Kitchen
The range, sink, refrigerator and cabinets (work center) are arranged along one wall.
Great for limited space
Very limited storage & countertop space
Notes: Advantages: All the appliances and food prep are easy to access, saves money and materials
Disadvantages: Least efficient plan, difficult for multiple people to use, lack of storage space, not for people who cook a lot

## Slide 7: One Wall Kitchens

## Slide 8: Corridor/Galley Kitchen
Appliance and cabinets are arranged along 2 walls, with an aisle between them.
Usually has a compact but efficient work triangle
Least desirable work triangle due to potential traffic interference
Notes: Advantages: everything is usually within arms reach, ideal for long and narrow spaces
Disadvantages: does not increase house value

## Slide 9: Corridor/ Galley
Notes: Observe how the microwaves in both kitchens are off the counter to allow for more counter space. The kitchen on the left is more narrow and would be hard for multiple people to cook at the same time. You would want to check clearances to see if you could open the bottom cabinets and still have 36” walk space. The kitchen on the right has a wider aisle, allowing for more people to be in the kitchen at one time.

## Slide 10: L-Shaped Kitchen
Appliances and cabinets are arranged along 2 adjoining walls. Allows an open area that may be used for dining.
More than 1 person can work in kitchen
Less efficient than other layouts
Uninterrupted work triangle
Notes: Advantages: good use of space, easily transformed with an island, simplifies cooking and clean-up, most versatile layout
Disadvantages: appliances far away from each other makes for a larger work triangle

## Slide 11: L-Shaped
Notes: L-Shaped kitchens sometimes allow for an eat in table to be placed in the room (depending on size of room and table). The distance between the two outside appliances will be greater. Again the more appliances you can get off the countertop the more prep room you will give yourself.

## Slide 12: U-Shaped Kitchen
Contains appliances and cabinets that are arranged along 3 adjoining walls.
Most efficient work triangle
The most desirable because most have more continuous counter and cabinet space than other layouts.
Notes: Advantages: great for a large family, lots of counter space, free flowing traffic, more room for organization
Disadvantages: can space out your work triangle, corner cabinets can be difficult to access

## Slide 13: U-Shaped
Notes: Pay attention to the counter space in both of these designs. The one on the right appears to have more work counter space and could probably work well with more than one cook. However look at the storage differences. Which kitchen do you think has more storage? Why? Not all u-shaped kitchens are large, some are very small, but would still give more counter sapce than a galley or one wall kitchen.

## Slide 14: Island
A freestanding storage and countertop unit added to a kitchen
Island can include chairs for eat in area
Best used in a one-wall or l-shape kitchen
Notes: Advantages: extra storage, can be used for cooking space, can add seating to a kitchen, some islands are movable and can be pulled in only when needed.
Disadvantages: Can be expensive to install, can interfere with traffic patterns.

## Slide 15: Island
Notes: In both of these pictures the island adds eat-in space to the kitchen as well as some prep space. Some people put part of the work triangle in the island, such as the cooktop or a sink. Islands are a great way to add more storage to a kitchen. Make sure you add proper lighting and check aisle depths before installing an island. You want to maintain your 42” clearance around all sides of the island.

## Slide 16: Peninsula
A kitchen countertop that is attached at only one end to a wall.
Usually cabinets beneath countertop
Often serves as an eating area
Notes: Advantages: extremely space efficient, creates visual separation between rooms
Disadvantages: can cause traffic blockage
Peninsula's can be used in l-shaped kitchens, u-shaped kitchens, or as a 4th wall in a kitchen. Make sure your clearance into the kitchen meets the 32” rule, 36” for ADA guidelines.

## Slide 17: Peninsula
Notes: Peninsula’s add great eat in sections in a kitchen. Make sure lighting is adequate in over the peninsula.

## Slide 18
Appliances

## Slide 19: Kitchen Sinks
Styles and colors to suit every style
Can be round, square, oval: deep or shallow
Can have single, double, triple bowls
Can be made of porcelain, stainless steel, acrylic

## Slide 20: Refrigerators
The type of refrigerator you need depends on your food habits.
Ask yourself: Do we cook most meals? Do we primarily use take out? Do we eat lots of fresh fruits and vegetables? Do we want cold drinks?

## Slide 21
Bottom Freezer: Refrigerator space is on top. Easy access to things you use more often. Variety of door options.
Side by Side: Freezer is to the left of the Refrigerator. Good for narrow kitchens. Easy access to both parts.
Top Freezer: Have to bend down to get food out of refrigerator.

## Slide 22: Ranges, Cooktops & Ovens
Range= surface cooking and ovens
Cooktop= surface cooking unit
Oven= single unit used for baking

## Slide 23: Electric Range
A range in which the heat for cooking
is provided through coils by electric power

## Slide 24: Gas Ranges
A range with gas rings and an oven for cooking with gas
Gas is controlled with a valve with electronic igniters (required by law)
You have to have natural gas source
Allows for more precise temperature control & more energy efficient than electric

## Slide 25: Induction Range
Heat through an electromagnetic field below the glass top.
Precise control over heat
Surface stays cool
Need special cookware
Can sometimes have a clicking sound

## Slide 26: Range Hoods
Contains a fan and hangs above a stove to remove fumes, smoke, odors, heat, and steam.
Standard range hoods are vented to the outside.
Range hoods with microwaves in them recirculate the air back into the kitchen.

## Slide 27: Conventional Ovens
Top and bottom burner, no fan

## Slide 28: Convection oven
Bake foods in a stream of heated air, uses a fan to circulate heat, browns
Cooks food faster at a lower temperature
Notes: Many double ovens put in homes today have one conventional and one convection oven. Toaster ovens are another example of convection ovens.

## Slide 29: Dishwasher
Saves time, energy & water.
Uses hotter water & stronger detergents, & dries dishes faster
Recommended to put within 36 inches of sink